# Slide 1:
I am going to present a paper titled “Design of a FFT/IFFT module as an IP core suitable for embedded systems”.

Firstly, I am going to begin with an introduction.
# Slide 2:
The objectives have been:
First, perform a comparison between three different methodologies:
VHDL coding, System-level tools at RT level, and System-level tools at macroblock level
Second, propose a general methodology that facilitate the design of this type of DSP functions as IP cores for embedded systems.
Turning now to the comparison of methodologies, ...
# Slice 3:
VHDL coding methodology consists of developing the module at RT level using direct coding in VHDL.
# Slice 4:
System-level tools at RT level methodology consists of design the module at RT level using System Generator for DSP.
# Slice 5:
System-level tools at macroblock level consists of modeling this module using the System Generator's FFT block.
Now I would like to describe the simulation process.
# Slice 6:
Designs have been simulated using Simulink and ModelSim in both M1 and M2 methodologies.
In the third methodology, design simulation is totally carried out using Simulink.
Besides, input stimuli have been generated using the Source Blockset of Simulink.
Next, I am going to present the simulation results.
# Slide 7:
As you can see from the table, M1 and M2 reduce the amount of clock cycles necessary to the calculation from 341 to 292 with respect to M3.
Besides, M1 and M2 reduce the output relative error from 5.09% to 0.59% with respect to M3.
Turning now to the hardware implementation results, ...
# Slide 8:
In a first approach, designs have been implemented on a Virtex FPGA, because System Generator's FFT macroblock only can be implemented in this type of FPGA.
As you can see from the table, M3 saves about 6-7% slices and achieves the highest maximum operation frequency with respect to M1 and M2.
# Slide 9:
In a second approach, designs have been implemented on a Virtex-II FPGA because this device has all the features necessary to implement DSP functions: embedded multipliers, block rams, etc.
As you can see from the table, results are very similar for both M1 and M2. Designs reach the same maximum operation frequency (40 MHz).
# Slide 10:
Next, Now I'm going to present a proposal of general methodology that combines both M1 and M2 and can be summarized as follows:
- Design the module with System Generator at RT level.
- Use VHDL coding for those blocks that are easier to program with such a language.
- Verify the module by HDL co-simulation.
This methodology:
- Facilitates the design and simulation processes.
- Allows designers to maintain total control over the module architecture.
# Slide 11:
Finally, lines of future work are:
Improve the module in order to make it fully configurable in terms of data width, symbol length, internal data precision, etc.
Optimize the design, reducing the hardware resources used and increasing the operation frequency.
Add an interface that allows its connection to a standard bus: OPB, APB, etc.